## Slide 1
eVance QA Server
AlarmNet Server
Distribution/Redirecting
Services
RAS Server
Integration Server
RAS Client
Consumer Module
Web API
Fire Panel with CCP
CCP
Fire Panel
…
High Level Architecture
ETW Applications &
Tools
User account based which expects User-ID & Password
No support for https (certificate)
Events with Unique Account-Code
Windows Event Tracing & Logging mechanisms
Fire Panel with CCP
CCP
Fire Panel

## Slide 2
Unique Account-Code for CCP
1
ESD
Customer N
Customer 1
…
Site 1
Site X
…
Download configuration to panel using SK Tools
…
Events Store for Panel M
……
Events Store for Panel 1
2
Upload configuration file to eVance services for generation of Account Code
3
Retrieve Unique 6-Byte ACCOUNT-CODE from eVance Server
4
Pushes Account-Code to Panel
AlarmNet Server
5
CCP sends Events with Account-Code to AlarmNet Server
SK Fire Panel with CCP
CCP
Panel 1
SK Fire Panel with CCP
CCP
Panel M
Integration Server
6
7
Silent Knight Tools
Use of SK Tools comes into picture for these operations
Redirects events to Integration Server
Sends events to eVance Server via Web-API that gets stored to respective event stores

## Slide 3
ESD downloads configuration to the fire panel using SK Tools
For the customers who are registered for eVance licenses, the ESD sends the panel configuration files to eVance services for generation of unique Account-Code for each panel.
Step 1
Unique Account-Code for CCP step-by-step
ESD
Silent Knight Panel
Silent Knight Tools
Step 2
Panel configuration
ESD
Panel configuration file
Unique 6-Byte Account-Code
The 6-Byte Account-Codes are pushed to the panels directly or through use of SK Tools
Step 3
ESD
Unique 6-Byte Account-Code
Silent Knight Panel

## Slide 4
CCP sends panel events with ACCOUNT-CODE to AlarmNet Server
Step 4
Panel events with Account-Code
contd…
SK Fire Panel with CCP
CCP
AlarmNet server redirects the events to an Integration Server
Step 5
Events of all panels (along with Account-Codes)
Integration Server
AlarmNet
Server
The Integration Server pushes the events to eVance Server through web API and the events are further stored into their respective panel event stores.
Step 5
Events of all panels
(along with Account-Codes)
…
Events Store for Panel 1
Web API
Events Store for Panel M
AlarmNet
Server
Integration Server